## Slide 1: Doppelgänger Testing for Autonomous Driving Software
Yuqi Huai*, Yuntianyi Chen*, Sumaya Almanee*,
Tuan Ngo+, Xiang Liao*, Ziwen Wan*,
Qi Alfred Chen*, Joshua Garcia*
Doppelgänger
* University of California, Irvine
+ VNU University of Engineering and Technology

## Slide 2
a second self or different version of oneself
a ghostly counterpart of a living person
Doppelgänger

## Slide 3: Autonomous Driving Software (ADS)
Ensuring American Leadership in Automated Vehicle Technologies: Automated Vehicles 4.0
MAR 2018
NOV 2021
a.k.a. autonomous vehicle
Promising benefits:
  Fewer crashes
  Increased mobility
  etc.
Safety concern remains.
Notes: https://www.nbcnews.com/tech/tech-news/self-driving-uber-car- hit-killed-woman-did-not-recognize-n1079281
https://www.cnbc.com/2021/12/14/california-halts-ponyais-driverless- testing-permit-after-accident.html

## Slide 4: ADS Testing
Simulation-Based
Does not require permit.
https://www.dmv.ca.gov/portal/vehicle-industry-services/autonomous-vehicles/autonomous-vehicle-testing-permit-holders/
Field-Operational
Requires Permit.
Notes: - 40 companies have permit for testing with a driver
- 7 companies have permit for driverless testing

## Slide 5: Related Approaches
AV-FUZZER (ISSRE’20)
MOSAT (FSE’22)
CRISCO (ASE’22)
AutoFuzz (TSE’23)
Common Aspects:
  Single AV and 2-4 obstacles.
  Focus on finding ADS collisions.
collisions

## Slide 6
Do all collisions effectively reveal ADS bugs?
collisions
revealing
bugs

## Slide 7: Scenario #1: Side-impact
The AV and the obstacle cruising side-by-side.

## Slide 8: Scenario #1: Side-impact
The obstacle forces a lane change.
The AV has the right-of-way, and the obstacle is fully responsible.
Does Not reveal an ADS bug.
No ADS misbehavior.

## Slide 9: Scenario #2: Left-turn
The AV and the obstacle are coming from different directions.

## Slide 10: Scenario #2: Left-turn
The AV turns left.
The obstacle has the right-of-way, and the AV is fully responsible.
Scenario reveals ADS bug.
ADS misbehavior exists.
responsible
reveals
misbehavior

## Slide 11
An ADS being responsible indicates its misbehavior, thus reveals an ADS bug.
responsible
revealing
misbehavior

## Slide 12: Determining Responsibility Is Hard
Police Citations
Insurance
Investigations
Lawsuits
https://www.forbes.com/advisor/car-insurance/determining-fault-after-accident/

## Slide 13: Determining Responsibility Naïve Approach #1: Experts On Call
bug_revealing = []
while True:
scenario = run_scenario()
if detect_collision(scenario):
if call_police(scenario) or \
call_insurance(scenario) or \
call_judge(scenario):
bug_revealing.append(scenario)
else:
print(“Not Bug Revealing!”)

## Slide 14: Determining Responsibility Naïve Approach #1: Experts On Call
bug_revealing = []
while True:
scenario = run_scenario()
if detect_collision(scenario):
if call_police(scenario) or \
call_insurance(scenario) or \
call_judge(scenario):
bug_revealing.append(scenario)
else:
print(“Not Bug Revealing!”)
Too Much Manual Work Involved!

## Slide 15: Determining Responsibility Naïve Approach #2: Improve Obstacle Modeling
Use a sophisticated obstacle modeling that:
  Drives realistically.
  Respects all traffic laws.
  Respects right-of-way rules.
  Reacts properly to other road-traffic participants.
  Never be responsible for causing violations.
Exactly the requirements an ADS should meet!

## Slide 16: Determining Responsibility Naïve Approach #2: Improve Obstacle Modeling
Use a sophisticated obstacle modeling that:
  Drives realistically.
  Respects all traffic laws.
  Respects right-of-way rules.
  Reacts properly to other road traffic participants.
  Never be responsible for causing violations.
Exactly the requirements for an ADS to be perfect!
Perfect Obstacles Does Not Exist Yet!

## Slide 17: Doppelgänger Testing

## Slide 18: Doppelgänger Testing
Let the ADS control every vehicle in the simulation!
If collision occurs, one of the AVs must be responsible, thus revealing a bug in the ADS.

## Slide 19: Doppelgänger Testing
Given the same scenarios ...
Prior Approach:
  Which car is the AV?
  Is it responsible?
Doppelgänger Testing:
  Which AV is responsible?
Doppelgänger
Testing

## Slide 20: DoppelTest
Doppelgänger
Testing
https://github.com/YuqiHuai/DoppelTest, https://zenodo.org/record/7657587
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
HD Map
Map Parser
Scenario
Generator
Analyzer
Recorded
Scenarios
Scenario Representation

## Slide 21
Analyzes HD Map used by the ADS.
Identifies:
  Valid locations of road-traffic participants.
  Conflicts between signals at every junction.
Doppelgänger
Testing
Map Parser

## Slide 22: DoppelTest
Doppelgänger
Testing
https://github.com/YuqiHuai/DoppelTest, https://zenodo.org/record/7657587
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
HD Map
Map Parser
Scenario
Generator
Analyzer
Recorded
Scenarios
Scenario Representation

## Slide 23: DoppelTest
Doppelgänger
Testing
Scenario
Generator
AV 1 (start, destination)
AV 2 (start, destination)
AV 3 (start, destination)
...
Pedestrian 1 (crosswalk)
Pedestrian 2 (crosswalk)
...
Traffic Signal Configuration (green/yellow/red-clearance interval)

## Slide 24: DoppelTest
Doppelgänger
Testing
https://github.com/YuqiHuai/DoppelTest, https://zenodo.org/record/7657587
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
HD Map
Map Parser
Scenario
Generator
Analyzer
Recorded
Scenarios
Scenario Representation

## Slide 25: DoppelTest
Doppelgänger
Testing
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
Manages AV instances.
  Initializing, resetting.
  Sending routing request.
Communicates with all AV instances.
  Retrieves their location.
  Exchange locations between AVs.

## Slide 26: DoppelTest
Doppelgänger
Testing
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
Translates ground-truth localization into ground-truth perception.
Narrows the focus to Prediction and Planning module.
Ensures scenario validity as long as AVs can ensure realistic movement.

## Slide 27: DoppelTest
Doppelgänger
Testing
https://github.com/YuqiHuai/DoppelTest, https://zenodo.org/record/7657587
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
HD Map
Map Parser
Scenario
Generator
Analyzer
Recorded
Scenarios
Scenario Representation

## Slide 28
Reports Violations
  Collision
  Red-light
  Stop-sign
  Routing Response
Analyzer
Doppelgänger
Testing
Analyzes
  Closest distance between road-traffic participants.
  Pairs of conflicting trajectories.
  Unique decisions made by each of the AV instances.
  Number of violations.

## Slide 29: DoppelTest
Doppelgänger
Testing
https://github.com/YuqiHuai/DoppelTest, https://zenodo.org/record/7657587
AV 1
Doppelgänger Orchestrator
Message
Broker
AV 2
...
localization
perception
HD Map
Map Parser
Scenario
Generator
Analyzer
Recorded
Scenarios
Scenario Representation
Notes: more details, including genetic representation, formalism will be discussed in the paper

## Slide 30: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Generated scenarios on Borregas Avenue with Baidu Apollo 7.0
Experimented for 240 hours

## Slide 31: DoppelTest Evaluation
Bug Description | Number
Failure to plan for slow dynamic obstacles. | 19
Failure to react to obstacle heading change. | 41
Incorrect prediction trajectory. | 12
Unsafe lane borrow decision. | 9
Improper overtake decision. | 2
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow

## Slide 32: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 1: Borrows lane to bypass AV 2.
AV 2: Idle.
AV 3: Idle.
AV 1
AV 2
AV 3
https://zenodo.org/record/7622399

## Slide 33: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 1: Plans to return to its original lane.
AV 2: Idle.
AV 3: Idle.
https://zenodo.org/record/7622399

## Slide 34: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 2: Moving forward.
AV 1: Yields to incoming traffic (AV 3).
AV 3: Moving forward. Sees AV 1 blocking the lane. Plans to borrow lane.
https://zenodo.org/record/7622399

## Slide 35: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 2: Moving forward.
AV 1: Yields to incoming traffic (AV 3).
AV 3: Moving forward. Sees AV 1 blocking the lane. Plans to borrow lane.
https://zenodo.org/record/7622399

## Slide 36: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 1: Returning to lane. Plans to overtake AV 2.
AV 2: Moving forward.
AV 3: Realizes it cannot borrow lane. Yielding to AV 2.
https://zenodo.org/record/7622399

## Slide 37: DoppelTest Evaluation
Doppelgänger
Testing
Evaluation
Case Study: Unsafe Lane Borrow
AV 1: Collision.
AV 2: Collision.
AV 3: Observing a BUG-REVEALING collision.
https://zenodo.org/record/7622399

## Slide 38: DoppelTest Evaluation
Bug Description | Number
Stop sign rolling stop. | 33
Ignoring traffic light. | 5
Routing failure. | 2
Doppelgänger
Testing
Evaluation
Case Study: Planning Module Ignores Red Traffic Signal

## Slide 39: Confirmed bugs and issues
Issue/14551 (Confirmed)
Issue/14550 (Confirmed)
Pull/14531 (Fix Accepted)

## Slide 40: Summary
Doppelgänger Testing
  Testing by observing the interaction between multiple instances of the ADS.
  Guarantees ADS being responsible for any violation occurring.
DoppelTest
  A framework that generates bug-revealing violations.
  Discovered 8 unique bug categories in an high-autonomy open-source ADS.
Thank you! Any questions?